## Slide 1: OLSBA Typical Septic System Abandonment & Sewer Hookups
December 2019

## Slide 2: Homeowner Responsibility - Sewers
It is the responsibility of the homeowner, at their expense, to connect their house to the sewer service stub at their property line and to abandon their septic system after the sewer system is installed, inspected and tested
If the property owner fails to connect to the sewer service stub, the WPCA shall cause the connection to be made and shall assess the expense to the homeowner
Fuss & O’Neill will assist homeowners to complete the Lateral Location Form to assist the property owner to place the sewer line stub at the property line for your property
Map for each property has been provided for homeowner to depict preferred location
The preferred location should
  Minimize disruption to plantings and driveways
  Identify any other conditions or concerns

## Slide 3: Public Health Code
Conn Public Health Code (Section IID) requires “Abandonment of subsurface sewage disposal system components (i.e. septic tank, hollow leaching structure) or cesspool shall be performed in such a manner as to eliminate the danger of inadvertent collapse of the component or cesspool. The responsibility for abandonment lies with the property owner. Structures that are to be abandoned shall be emptied of all sewage prior to abandonment. Structures shall be filled with sand, gravel, or crushed and backfilled with clean soil.”
Property owners are required, at their expense, to abandon their Septic Tank at the same time the sewer connection to their house is completed.

## Slide 4: Problem with Old Septic Systems
Connecticut Public Health Code states responsibility lies with the property owner to eliminate the danger of inadvertent collapse 1
Forgotten septic tanks, hollow leaching structures, cesspools, and drywells present serious hazards including cave-in or collapses and asphyxiation hazards.
It is unwise to leave a potentially lethal hazard and personal liability unaddressed at your property.
1 Public Health Code Technical Standards for Subsurface Sewage Disposal Systems - Section IID

## Slide 5: What is the Homeowner’ Responsibility?
Owners shall abandon septic systems when a public sewer becomes available
Work needs to be done by an experienced contractor who knows proper safety procedures
Pumping septic system waste into a public sanitary sewer system is prohibited

## Slide 6: Quick Reference - Septic System Abandonment
Source: onsiteinstaller.com

## Slide 7: Best Practices for Septic System Abandonment
Notify WPCA and Local Health Department (Ledge Light Health District) as required
Disconnect power at the source to all electric controls and remove all controls and panels (if applicable)
Pump out the septic tank and any hollow structures by a Licensed Septic Hauler. Do not pump the contents into a public sewer
Remove tank cover
Rupture bottom of structure (after pumping) to prevent retainage of water
Take photo of structure (before filling)
Fill structures with sand, gravel, flowable fill, or crush & backfill with clean soil
Take second photo after filling to the top of sidewalls
Use sand, aggregate, and soil from mound to fill the tanks if a mounded system is being abandoned
Compact material to prevent settling
Disconnect and seal all piping leading to/from the structure
Grade site and establish vegetative cover
Document the location and methods of the filled-in septic system so future site workers can anticipate these buried obstructions
Submit a copy of the pumping receipt, filled-in tank location, and photos to the Local Health Department (Ledge Light Health District) to record abandonment

## Slide 8: Best Practices for Septic System Abandonment
Crush Tank Cover
Fill with sand or gravel & compact well
Pump out tank contents
Rupture tank bottom
Disconnect All House Piping
Submit documentation to Local Health Department when complete
Document work with Photos, Measurements, and Receipts

## Slide 9: Typical Water Service and Sewer Lateral Plan OLSBA
Association Right-of-Way
Water Meter
Mainline
Water
New/Replace-ment
Water Service
W
W
W
Homeowner’s Responsibility
10 Foot Min.
Separation
Association’s Responsibility
x
Curb Stop

## Slide 10: Water Connections
The CT Water Co will be furnishing and installing year-round water mains and fire protection in 2020.
For CWC’s existing customers, CWC will connect the new system to the homeowner’s existing seasonal service connections at their property line. Seasonal service will be uninterrupted.
For those houses that are not current customers CWC will install only the laterals and curb stops to the property line
Houses that have wells and no CWC service do not have to connect to the CWC system.
Houses without CWC service who want to have year-round water service must complete a CWC application and conform to their terms and conditions and will be responsible to connect at their own expense from the curb stop to the house.

## Slide 11: Typical Blank Lateral Location Plan

## Slide 12: Typical Sewer and Water Lateral Location Form Legend

## Slide 13: Typical Lateral Location Form Instructions
* Costs for water service lateral from
property line to the building shall
be borne by the Homeowner for
those homeowners that do not
have water service.
*

## Slide 14: Example Sewer and Water Lateral Location Form
10 feet
Preferred water service location can be
provided for those that do not currently have
water service. All costs for services from
the property line to the home shall be borne
by the Homeowner. If existing well on property
Is to remain, a backflow preventer needs to be
Installed at the homeowner’s expense.